## Slide 1: EPT-Based Sub-Page Protection On Xen
Yi Zhang <yi.zhang@intel.com>
Notes: Today, we are going to introduce the EPT-based sub-page protection on Xen which called SPP for short.

## Slide 2: Agenda
Overview
Implementation
User Cases
Q/A
Notes: We will high level introduce the SPP in the section 2 - Implementations, and give it's overall pictures.
In Section 3 we will take 2 user cases for examples. depth explanations it's usage. like.. security, and hardware specific usages
Intercept me if you have any questions

## Slide 3: SPP Overview
EPT-Based Sub-Page Protection (SPP)
- Allow write-protecting guest physical memory at a sub-page (128byte) granularity
4K Page
Original Page
Write-Protection
Granularity
EPT-Based SPP
With SPP
128 byte
···
32 × 128 byte
Sub Pages

## Slide 4: Implementation
Sub-page protection overall picture
Sub-page permission table
Sub-page permission table pointer
Sub-page permission table induced VM Exit
Sub-page permission table capability
Sub-page permission table enforcement
Hypercalls to set/get Sub-Page Write Protection

## Slide 5: How SPP Works:
Guest Physical Address
(GPA)
Original EPT:
EPT-Based SPP
Walk EPT
1
EPT leaf entry
Writable?
Y
N
Write access to page
Write access deny
GPA
Walk EPT
1
1
61
EPT leaf entry
Writable?
Y
Write access to page
Walk SPP Table
SPP table pointer
in VMCS
1
0
0
1
63
···
2
128 byte
128 byte
···
Physical Page
Allow
Deny
SPPT L1E format
0+2i : sub-page write access
1+2i : reserved
1
N
VM_exit

## Slide 6: Sub-page Permission Table (SPPT)
Sub-page Permission Table
  4-level paging structure
  Set up by hypervisor
  Walked by hardware
Sub-page Permission Table Pointer
  64-bit control field on VMCS
  Point to the SPPT L4 table

## Slide 7: Sub-page Permission Table (SPPT)
Most like EPT table, the SPPT L4E L3E L2E format are defined as below figure:
| :------------------ | :-------------------------------------------------------------------------------------------------------- |
| Bit | Contents |
| :------------------ | :-------------------------------------------------------------------------------------------------------- |
| 0 | Valid entry when set; indicates whether the entry is present |
| 11:1 | Reserved (0) |
| N-1:12 | Physical address of 4K aligned SPPT LX-1 Table referenced by the entry |
| 51:N | Reserved (0) |
| 63:52 | Reserved (0) |
| :------------------ | :-------------------------------------------------------------------------------------------------------- |
The SPP L1E format is defined as below figure:
| :------------------ | :-------------------------------------------------------------------------------------------------------- |
| Bit | Contents |
| :------------------ | :-------------------------------------------------------------------------------------------------------- |
| 0+2i | Write permission for i-th 128 byte sub-page region. |
| 1+2i | Reserved (0). |
| :------------------ | :-------------------------------------------------------------------------------------------------------- |
Note: `0<=i<=31`

## Slide 8: Sub-page permission table induced VM Exit
An SPPT paging-structure entry contains an unsupported value during SPPT lookup.
SPPT paging-structure entries are not present during SPPT lookup.
SPP Misconfiguration
SPP Miss
EPT violation VM Exits due to SPPT
Memory writes that consult but are not permitted by the SPPT cause EPT violations normally.
NOTE
SPP Vm Exits reason value is 66.
SPP Misconfiguration and SPP Miss Vm Exits can be told by exit qualification bit 11, set for SPP Miss, cleared for SPP Misconfig.

## Slide 9: Sub-page Permission Table View
SPPTP
SPP miss
SPP missconfig
setup spp table
0
EPT violation
not present
unsupported value

## Slide 10: Sub-page permission table capability
IA32_VMX_PROCBASED_CTLS2
Secondary Proc-Based VM-Execution Controls
MSR 0x48b
0
31
23
SPP Bit
Capability on VMX MSR
Enabling on VMCS Control fields
bit [23] = 1
SPP is globally enabled

## Slide 11: Sub-page permission table enforcement
Bit 61 of an EPT PTE is changed to “Sub-Page Permission” (SPP bit).
Setting this bit allows write permissions for the page to be enforced on a sub-page basis .
EPT leaf paging-structure entries
63
61
physical address of page
N-1
12
0
2
SPP
physical page
Set to act on

## Slide 12: Hypercalls to set/get Sub-Page Write Protection:
Defined 2 hypercalls to set/get subpage write protection bitmap per gfn, each gfn corresponds to a bitmap.
The host management application, qemu, or some other security control daemon. will set the protection bitmap via this pair of hypercall.

## Slide 13: User Case Ⅰ
Security data structure protection
4K Page
Allocated User Data
U32 Protected_bitmap
User ID
Un-Protected
Protected
32 × 128 byte
Sub Pages
Private Key
Mobile Number
Public Email
Billing Infor
Name
…
Protected
Un-Protected
Un-Protected
Protected
Un-Protected
Origin 4K page

## Slide 14: User Case Ⅰ
VM
4K Page
User ID
Private Key
Mobile Number
Public Email
Billing Infor
Name
…
Origin 4K page
EPT table
SPP table
Client
write
Approve
VM Exit
VMM
HPA
User ID
Security check
Denied
write

## Slide 15: User Case Ⅱ
Device mmio space protection
4K Page
A Pass-through
dev mmio space
U32 Protected_bitmap
Sensitive Reg Set[0]
Un-Protected
Protected
32 × 128 byte
Sub Pages
Sensitive Reg Set[2]
Public Reg Set[...]
Public Reg Set[3]
Sensitive Reg Set[31]
Public Reg Set[1]
…
Protected
Un-Protected
Un-Protected
Protected
Un-Protected
4K mmio space

## Slide 16: User Case Ⅱ
MMIO
Space
sensitive register set
public register set
Device
EPT table
SPP table
public register set
sensitive register set
Host
Direct assign
Device
GPA
VM
Approve
Trap & Emulate
VM Exit

## Slide 17: Resource
Intel SDM:
https://software.intel.com/sites/default/files/managed/c5/15/architecture-instruction-set-extensions-programming-reference.pdf
Xen Patch link:
https://lists.xenproject.org/archives/html/xen-devel/2017-10/msg02215.html
KVM Patch link:
https://lkml.org/lkml/2017/10/13/460

## Slide 18: Q & A